## Slide 1: Design for X and Prototyping at RPI
Mark Anderson,
IED Course Coordinator
Sr. Project Engineer, SoE
Aren Paster
Project Engineer, SoE

## Slide 2: Learning Objectives
Gain an awareness of prototyping capabilities available to SOE students
Gain an awareness of DfX strategies and outcomes.
Apply basic DfX guidelines to a “simple” problem.

## Slide 3: Prototyping at RPI
Fabrication Assistance
  Conventional Machining
  CNC Plasma Cutting
  CNC Abrasive Water-Jet
  3D Printing
  Electronics
Architecture Wood Shop
Supplies

## Slide 4: Prototyping at RPI
Resources
Student Machine Shop – JEC 1010
    Mr. John Szczesniak x6551
    CNC Plasma Cutting and Turning
    Conventional Machine Tools
    Welding (steel and plastic)
    Laser Cutter
IED Fabrication Area – JEC 2332
    Electronic Instrumentation & Basic Components
    Conventional Machine Tools & Hand Tools
    Open hours posted on door and LMS

## Slide 5: Prototyping at RPI
Resources
Douglas Mercer ’77 Laboratory – JEC 6204
    Prof. Mona Hella, hellam@ecse.rpi.edu x6314
    Soldering/assembly space
    Manual pick and place, Printed Circuits Board (PCB) population
    4 test benches with various electronic test equipment & specialized equipment
    Environmental chamber
    Parts room (free electronics parts and a storage area for student projects)
    Open hours: weekdays + Saturday afternoon

## Slide 6: Prototyping at RPI
3DPrinting and AWJ
  3D Printing
    E-mail – 3Dprint@rpi.edu
  Abrasive Water-Jet Cutting
    E-mail - AWJlaser@rpi.edu
  Forms
    LMS
    HUB
    http://manufacturing.eng.rpi.edu/
Supplies
  Student Machine Shop
  R&D Shop – Science Center Basement
  Plastic Stock in IED Fabrication Area
  See LMS Technical Resources -> Manufacturing resources.pptx

## Slide 7: Prototyping at RPI
Forms available on the Manufacturing Network Site

## Slide 8: Prototyping at RPI
Manufacturing Network Webpage
  http://manufacturing.eng.rpi.edu/
Manufacturing Resources List on LMS
  Local & on-line material and parts suppliers, on-campus contacts
    Technical Resources ›
      Manufacturing_resources.pptx
      Manufacturing Services Overview

## Slide 9: If you want a Rapid Prototype or Waterjet cut part, just…
A – stop by the machine with an idea, we’d love to show you how to operate the equipment
  B – sketch your part and talk to your section instructor
C – email CAD file (.DXF or .STL) to 3Dprint@rpi.edu or AWJlaser@rpi.edu for price quote
D – get form from Sam Chiappone

## Slide 10: Design for X
Under the label Design for X, a wide collection of specific design guidelines are summarized. Each design guideline addresses a particular issue that is caused by, or affects the characteristics of a product. […]Thus, it is not granted that a freshman or someone who is outside of the subject area will comprehend this generated explicit knowledge.
 | This article is incomplete. Please help to improve the article, or discuss the issue on the talk page. (February 2009)
Wikipedia, 10/23/13
DFX means design for excellence, and also "design for X", where X is a variable with many values

## Slide 11: Function : Provide Light
Notes: Flashlight - http://www.maglite.com/D_Cell_LED.asp
Spot light - http://www.wycokck.org/InternetDept.aspx?id=19960

## Slide 12: Forks
Antique silver - $440
$220/ea
18/0 Stainless Steel - $14.97 for 4 place settings (20 pcs) $0.75/ea
Plastic – $3.79 for 100 pcs
$0.04/ea
18/8 Stainless Steel - $400 for 12 place settings (65 pcs) $6.15/ea
Notes: Silver - http://www.leopardantiques.com/object/image/download/9/Antique%20Silver%20Christening%20set%20(Nursery%20rhyme)_Hey%20diddle%20spoon%20and%20fork%20set.Jpg
18/0 – Walmart.com low price stainless
18/8 – Macys.com high price stainless – expensive silver set is $18,300 for 66 pcs -> $277/ea

## Slide 13: Product Difference?
Hamburgers
Operating
Systems

## Slide 14: Bicycle Comparison
Serotta Legend
Next Mountain Bike

## Slide 15: How many Next Amplifier 26” Men’s bikes does Walmart sell per year in the US?
A – 3,500
B – 50,000
C – 200,000
D – 1,000,000
E – 5,000,000
Notes: 2014 – 4,203 US stores
1/week * 52 weeks * 4203 stores = 218,556

## Slide 16: Bicycle Comparison
Next
$100
Front suspension
38 lbs
Steel
3 sizes – 20”, 24”, 26”
One
4,400
5,200
200,000+
Serotta
$5000
Carbon fiber rear stays
17 lbs
Titanium & Carbon Fiber
infinite choices - rider customized
32 paints, 6 decals
73
19
2,500-3,500
Price
Features
Weight
Material
Available sizes
Available colors
US stores
International stores
Volume/yr

## Slide 17: Market Comparison 2009 Data National Bike Dealers Association - http://nbda.com/articles/industry-overview-2009-pg34.htm
Manufacturing | US | Import
Volume | 276,000 total all sizes | 14.9 million – total 10.2 million - adult 20”+
Average price | $478 | 
Sales | Specialty Store | Mass Merchandiser
Volume share | 27% | 73%
Dollar share | 68% | 32%
Average price | ~$350 | $78
Notes: Import – China & Taiwan
US – approx 100 brands
$350 from Larry Ruff

## Slide 18: What makes these different? Consumer
$5000 Serotta bike
Material
  Titanium
  Carbon fiber
Performance components
Performance
  Weight
  Comfort / response
Rider customization
  Appearance
  Size
Brand Recognition
$100 Walmart bike
Material
  Carbon steel
Commodity components
Delivery
Notes: Ti tube - $46/ft ($275), CrMo tube - $8/ft ($50)

## Slide 19: What makes these different? Production
$5000 Serotta bike
Low volume
  Order process
  Cycle time
Manual process
  Weld
  Paint
  Manual and CNC machining
  Inspection
Fully adjustable tooling
Manufacturing tolerances
Packaging
$100 Walmart bike
High volume
Automated process?
  Weld
  Paint
  CNC machining
Standard jigs and fixtures
Notes: Serotta aligns to 6 times industry standard
± 0.5mm = 0.020”
Delivery 4-5 weeks from initial order placement

## Slide 20: Design for “X”
Performance
Overall features
Reliability
Serviceability
Environmental impact
Conformance to a standard
Manufacturability (chapter 11 in textbook)
Durability
Aesthetics
Perceived quality
Notes: - Chinese batteries added sand for weight

## Slide 21: Design For Manufacturing Defined
Manufacturing cost reduction begins at the design phase of a product.
Design revisions are made in an effort to reduce part count or complexity to eliminate non-value added elements of a component, subassembly, and/or final assembly.
Overall quality is not compromised as a result of the reduced costs.
Reduced costs = higher profit margins

## Slide 22: Design for Manufacturing Process Steps
  Evaluate Manufacturing and Assembly Processes and Operations
  Reduce manufacturing costs
  Reduce cost of components (Suppliers)
  Reduce the cost of assembly
  Reduce the cost of support operations

## Slide 23: Guidelines for Reducing Manufacturing Costs
  Component costs
    Make or buy
      Make – Design and build from raw material
        Costs = Labor, equipment, tooling
        In-house vs. supplier
        Material selection
        Tolerances
      Buy – vendor – standard items (nuts, bolts, motors, gears)

## Slide 24: Reduce Assembly Costs
Eliminate nonessential parts
Optimized Part Count Benefits Include
  Reduced Weight
  Reduced Complexity
  Reduced Opportunity for Error
  Reduced Assembly Time

## Slide 25: Step 3 – Reduce Assembly Costs
Eliminate nonessential parts
    Integrated part - Can the part be combined with another part?
      Inset molding a metal bracket in the plastic injection molding process could eliminate a fastener, assembly process, and potential point of failure.
        No assembly
        Reduced tooling/processing
        Assist in quality specifications (orientations are set)
Notes: Insert - http://img.directindustry.com/images_di/photo-m2/threaded-insert-for-plastic-422065.jpg
Plastic part - http://www.awi-industries.com/image/INJECTION_MOLDING_insert.jpg

## Slide 26: Guidelines for Reducing Assembly Costs
    Part inserted from top axis (Z) – top down assembly
    Self alignment features
      Tapers and chamfers
    No orientation required
      Phillips head screw – aligned with driver bit
    One hand assembly
      Less time, availability of the other hand to do another task
    No tools required for assembly
      Reduce the number of snap rings, cotter pins, springs, bolts/nuts
    Use Single motion assembly items
      Pins and snap-fits
    Integrated part - Can the part be combined with another part?
      Inset molding a metal bracket in the plastic injection molding process could eliminate a fastener, assembly process, and potential point of failure.
        No assembly
        Reduced tooling/processing
        Assist in quality specifications (orientations are set)
    Secure part with single motion
      Press fit

## Slide 27: The key to Design for Manufacture is:
    Low # of materials (Hoover Dam – concrete & rebar)
    Reduce skilled labor (Pyramids of Giza)
    Loose tolerance requirements (Great Wall of China)
    No tools required (Lego automobile)
    Reduce component cost (Pig’s straw house)

## Slide 28: Perceived Quality
Aspects
  Actual quality
  Parent brand image & history
  Scarcity / exclusivity
“Made in USA”
  Troy-Bilt
Cars - % retained value
  Lexus vs Altima commercials
Notes: Chinese batteries added sand for weight
Troy Bilt – bought by MTD in 2001
  FIRST Lexus - http://www.youtube.com/watch?v=AktHnnA9QIM
SECOND (response) Nissan - http://www.youtube.com/watch?v=6sr3Rh7Yjnc

## Slide 29: Customization
Fitted Hats
Laptop Skins
Serotta Personal Fit system
Notes: 25 paint colors, 30 decal colors, 7 different decals -> billions of combinations!
Fitted 6-3/4 through 8 in 11 choices. One size fits most 7-1/8 through 7-3/4 or 5 choices

## Slide 30: Performance
Aspects
  Features
  Test results
  Material properties / manufacturing process
  Tolerance
  Upper limits of design application
Alienware Computers

## Slide 31: Sustainability
Aspects
  Recyclability
  Carbon footprint
  Renewable material

## Slide 32: Design for ??
Legos
  167 pcs
K’Nex
  475 pcs
Notes: Legos – dozen sets, always EXTRA, but small pieces
K’Nex – 3 boxes, 300-500 pieces, always PERFECT

## Slide 33: Did actual # of pieces inside the box match claimed contents?
Lego – Yes. K’Nex – No.
Lego – No. K’Nex – Yes.
Both – No.
Both – Yes.
Inconsistent results, wouldn’t be appropriate to generalize.

## Slide 34: Team Exercise
Work in your project teams (15 mins)
Develop a conceptual design for a vehicle based on Design for “X”
  Standard features
  Option packages
  Six specifications and target values
Sustainability(left), Performance (center), Perceived Quality (right)