## Slide 1: Jeremy Laflin Lecturer, MANE Rensselaer Polytechnic Institute
Introduction to Engineering Design
Applications of Basic Machine Elements

## Slide 2: Today’s Objectives
Provide some basic analysis concepts to help increase your team project success
Make you think about way to apply basic analysis to your project
Make you aware of some basic mechanical elements that can be used in your project

## Slide 3: Today’s Agenda
Fasteners
Structural support
Transfer of rotational motion
Analysis
  Planning motion
    Mechanism design example
  Failure
    Catastrophic
    Performance out of spec.
Basic Mechanical Elements
Application of Mechanics

## Slide 4: iClicker Question
Do you intend on building anything for your team project ?
A) Yes B) No C) What team project ? D) What was the question ?

## Slide 5
O(105)
Mechanical Elements: Attachment

## Slide 6
O(105)
Mechanical Elements: Structural Components

## Slide 7
O(105)
Mechanical Elements: Rotational Motion

## Slide 8: Mechanical Elements: Where To Get Materials?
http://www.mcmaster.com/
http://www.mscdirect.com/
http://www.globalspec.com/
http://www.mpja.com/
www.smallparts.com
https://www.grainger.com/
Local Options
Harbor Freight (Albany)
Grainger Industrial Supply (Albany)
Pfeil Hardware (Troy)

## Slide 9: Group Exercise: Design a Mechanism That Takes Rotary Input and Transforms it to …
  Left: Intermittent Rotary Motion
  Middle: Reciprocating Translational Motion
  Right: Continuous Translational Motion
  1) Sketch an example mechanism (2 min) 2) List important engineering design considerations (1 min) 3) List prospective uses (1 min) 4) Come down and discuss (1 min)

## Slide 10
O(105)
Mechanisms: Transforming Motion

## Slide 11: Analysis Example: Gravity Powered Walker

## Slide 12: Analysis Example: How to Design Mechanism Motion

## Slide 13: iClicker Question
How many analysis-based courses have you taken at RPI ?
A) 1 B) 2-3 C) 4-6 D) > 6

## Slide 14: Analysis: Why ?
Sometimes failure has human consequences
Prototyping is expensive
Prototyping is not possible

## Slide 15: Analysis: Predicting Failure
Defining Failure
  Mechanism no longer performs within design specifications
    Change in material properties
  Catastrophic Failure
    Component(s) break

## Slide 16: Analysis: Failure to Perform Task
Environmental considerations
  Temperature (metal, plastic) / Humidity (wood)
    Change in component dimension / material properties
Fatigue
  Cyclic loading
Buckling

## Slide 17: Analysis: Component Failure
Determine external stress (applied forces)
Determine internal loads (thermal, friction)
Free Body Diagram (FBD)
Start with simple reduced model
  Increase complexity as necessary

## Slide 18: Analysis: Free Body Diagram (FBD)
Not complicated or cluttered (idealized)
Simply display relevant information

## Slide 19: Analysis: Statics
Often the starting point for analysis
Recall method of joints and sections
Recall assumptions: weight neglected, axial forces only
Get reaction forces at joints
  What size bolts do I need?

## Slide 20: Analysis: Strength of Materials
  Does it move out of spec ?
  Does it break ?

## Slide 21: Analysis: Strength of Materials
What about bending ?

## Slide 22: Analysis: Strength of Materials
  What about bending ?
  Compute total stress due to axial loads and bending.

## Slide 23: Analysis: Component Failure
Most things fail in shear
Not likely to fail due to normal stress

## Slide 24: Analysis: Structural Failure
Consider reaction forces
Consider bending
Determine stress in structural components
Does it break ?
  Yield stress important
Does it buckle ?

## Slide 25: Analysis: Structural Failure
Does it buckle ?

## Slide 26: Analysis: Structural Failure
Does it break ?
  What material should I pick ?
Does it buckle ?
  What material should I pick ?

## Slide 27: Analysis: Structural Failure

## Slide 28: Analysis: Dynamics
Now inertial forces matter
Methods of solving kinetics problems
  Direct
  Work-Energy
  Impulse-Momentum

## Slide 29: Analysis: Direct Method for Kinetics
Make a FBD
Solve forward problem (determine acceleration) or solve the reverse problem (determine forces) ?

## Slide 30: Analysis: Direct Method for Kinetics
How do we compute acceleration ?
?
  What is this equation for ?

## Slide 31: Analysis: Work Energy for Kinetics
What is the difference in these equations ?
Often used to determine some velocity change
Could be used to compute force required to stop an object

## Slide 32: Analysis: Impulse-Momentum
What if energy is not conserved and I don’t want to use the direct method ?
Often do not know force as a function of time on a particular component (look at system)

## Slide 33: Analysis: Dynamics
If your project is dynamic by nature
  Consider dynamic stability
  Consider vibrations
  Consider controls

## Slide 34: Analysis: Avoiding Failure
Does it move ?
  Should it ?
    Statics or Dynamics Analysis
Does it break ?
Does it buckle ?
Does it stop working ?
  Change in dimension ?

## Slide 35: Analysis: Prototype
Probably not subject to actual loads
Your engineering analysis should show that your prototype should not break, or fail
The analysis you deliver should also show that your actual design should not break, or fail

## Slide 36: Analysis Example: Performance
Did you make a Trebuchet for the mini-project ?
What is doing work ?
  What happens if the work done on the weight is minimized in the x-dir ?
    How: Eliminate side to side motion of the weight
Result is larger change in kinetic-energy