## Slide 1: Completing fragmentary river networks via induced terrain
Tsz-Yam Lau and W. Randolph Franklin
Rensselaer Polytechnic Institute
Troy NY 12180
partially supported by NSF grant CMMI-0835762
Notes: In this presentation, I am going to talk about a new approach of completing fragmentary river networks, which we name the induced terrain approach.

## Slide 2: Input: Fragmentary river segments
Original network
River segments
Notes: First let’s look into the problem in detail. On the left of this slide, you can see an example of what we have: a fragmentary river network. The black dots here represent observed river locations. They are in the form of broken line segments. What we need to do is to join these broken pieces together to form a complete river network, the one on the right. By a complete river network we usually assume it consists of a number of tree structures, each of them has no closed loop. Also, every river location has a way out to either the edge, or some particular sink inside the terrain.

## Slide 3: Why such input?
Notes: But why do we have such a problem? Why do we have that sort of data? That’s because of cloud covers and tree canopies, blocking the view of overhead surveys done on the aeroplanes and satellites.

## Slide 4: We need connections!
Key: connection
How to reach the ocean?
Where to flood next?
My next target?
Notes: That’s why we get only the fragmentary river segments but not the whole river network. To make use of these partial data in transportation problems, like planning ship routes, or foreseeing flooding area, or predicting the forthcoming target locations of the pollutants, we need to link the river segments appropriately.

## Slide 5: Induced terrain solution framework
Follow the constraints imposed by the given height.
  No connection if a hill is in between two river segments.
Notes: By appropriately we mean we have to take care of one important constraint – the set of heights. They are usually obtained alongside with the river locations. These height data may hint whether the river pieces should be connected. For example, a hill in between some two river segments may suggest that these two pieces should not be connected even though they are very close.
To incorporate these height information in river segment reconnection, we propose the induced terrain solution framework shown on the right of this slide. This framework involves two key steps. First we reconstruct a terrain using partial heights and river locations, and then we derive a river network of that induced terrain. Since the river network is derived from a terrain that is reconstructed based on the given heights, it is likely that that particular river network respects the constraints imposed by the partial observations.
In the following, I’ll concentrate on the implementation details of these two key steps.

## Slide 6: Hydrological corrected terrain reconstruction
Goal: Model the terrain based on given heights and river locations
  Two strategies
    General terrain reconstruction -> surface reconditioning
      General reconstruction: spine-fitting, ODETLAP, natural neighbor
      Surface reconditioning – stream burning, AGREE.aml
      Software package: ANUDEM – massage the terrain so it matches the complete river network observations
    Terrain reconstruction that is aware of river locations
      Hydrology-aware ODETLAP
T. Y. Lau & R. Franklin. Completing River Networks With Only Partial River Observations via Hydrology-aware ODETLAP. In 20th Fall Workshop on Computational Geometry, Oct 29-30, 2010.
Notes: So here is the first step: hydrological corrected terrain reconstruction. The inputs are the partial heights and river locations observed across the terrain. Our goal is to reconstruct a terrain that is compatible with these partial observations. The more information we can make use of from these partial observations, the much closer the terrain model is with respect to the original one, and hence the better subsequent river derivation that aims to recover the original river network.
There are two possible approaches to do this task. Approach number 1 is a two-step procedure, first applying some general terrain reconstruction scheme that works with the partial heights alone, like spine fitting, natural neighbor and ODETLAP, to generate a preliminary terrain surface. By this first step we produce a terrain that honors the given heights. After that we apply some surface reconditioning scheme to lower the given river locations, like stream burning. We may choose to lower their neighbors as well, like AGREE.aml. With this second step we effectively model the river locations as local minima with respect to non-river locations, something that we expect for a real river location. Indeed the famous software package ANUDEM is using this strategy to massage terrain surfaces to make them match the corresponding complete river networks better.
When we know something is currently done in two steps, we always ask if we can combine them. Approach number 2 is exactly this, we consider both heights and river locations at the same time and generate a hydrology-aware terrain directly. This is a rather novel approach and the only scheme we know to-date is the hydrology-aware ODETLAP, which we introduce in a recent workshop last month.

## Slide 7: Hydrological corrected terrain reconstruction - results
Dependent on how height data are distributed, and the speed needed
  Evenly-distributed height samples
    Natural neighbor with stream burning often offers best one-pass result.
  Height samples available at given river locations only (or even no height samples are available)
    Hydrology-aware ODETLAP outperforms others.
T. Y. Lau & R. Franklin. Completing River Networks With Only Partial River Observations via Hydrology-aware ODETLAP. In 20th Fall Workshop on Computational Geometry, Oct 29-30, 2010.
Notes: Just now we have seen the numerous possible combinations for the same task. We have tried all these combinations, and found out that which one to use depends on how the height samples are distributed, and the speed that we wish.
In particular, if height samples are evenly distributed across the terrain, as happened when cloud and canopy covers are rather evenly distributed, approach number 1 with natural neighbor interpolation and stream burning offers a good balance between accuracy and speed. However, if height samples are available at the river locations only, or worse still we have no height sample, hydrology-aware ODETLAP gives superior results.

## Slide 8: Terrain reconstruction (Evenly-distributed height samples)
Given river locations
NNSB error: 2.48%
SFSB error: 2.88%
OSSB error: 2.47%
NN-AGREE error: 2.44%
ANUDEM error: 3.82%
Original network
Notes: For details of the second case please refer to our another paper. Here I will focus on the first case. This slide shows the original river network, the given partial river network, and the reconstruction results with different hydrological corrected terrain reconstruction schemes. NNSB means natural neighbor stream burning that we recommend. SFSB means secondary spline fitting-stream burning, while OSSB means overdetermined system-stream burning. SFSB and NNSB are similar in the sense that they are parameter-less, while OSSB has one key factor to optimize. They are here to compare different general terrain reconstruction schemes. Next we have NN-AGREE that lowers the given river locations together with their neighbors as well. It is to check the effect of an alternative hydrological correction scheme. Finally we have the famous ANUDEM that is designed to massage terrains to match the given complete river network. Here we see if it works well with only partial river network data.
Indeed, different approaches feature different sets of correct reconnections. Sometimes it is hard to say from the figures which one is better. So we introduce a metric called river/non-river classification error to quantify the reconnection quality. The larger the error, the worse is the scheme in inducing a terrain that deduces the same river network as the original terrain. The percentage underneath each figure tells you the respective percentage error.
Obviously, ANUDEM is rather significantly outperformed by the other approaches.

## Slide 9: Terrain reconstruction (Evenly-distributed height samples)
Notes: And it is the same case when we look into the error figures of some other terrain sets. When comparing the two parameter-less general terrain reconstruction schemes SF-SB and NN-SB, SF-SB consistently performs worse than NN-SB. Another general terrain reconstruction scheme, OS-SB, consistently outperforms NN-SB. And we sometimes obtain better results by lowering the neighborhood of given river locations, as shown in the NN-AGREE columns. However, to achieve such performance, we need to adjust for optimal parameters, the smoothness-accuracy factor for OS-SB and the sink width for AGREE.aml. This means we have to compute a number of terrains under different parameters, which may not be affordable if the dataset is massive.

## Slide 10: Terrain reconstruction (Evenly-distributed height samples)
Findings
  Stream burning which lowers the elevation at exactly the river locations only offers better results than schemes that lower the neighborhood as well.
  Although complicated schemes like ODETLAP offers better result, they rely on iterative processing for optimal parameters. Natural neighbor interpolation and stream burning is the only one-pass approach known to-date that offers reasonably good results.
Notes: This is the summary of why we propose NNSB as the cost-effective solution in this case.

## Slide 11: Biased river derivation - Motivation
Not all given river locations remain their river status when the original river derivation scheme is applied to the induced terrain.
Notes: Now we go to the second step: deriving the river network from the induced terrain. A typical river derivation process involves first identifying the water flow direction of each location, and then we assume each location receives the same amount of water, and find out how much water will flow through the locations according to the flow grid. Those locations with water amount exceeding certain threshold value form the preliminary river network. Very often we are interested in the central lines of the river network, so we apply some skeletonization algorithm at the final stage to make sure the river network is one-cell thick.
Note that in the previous flow chart, we have the term “biased”. Why? It is because not all given river locations preserve their river status if the original river derivation scheme is applied to the induced terrain. The figure on the right illustrates this phenomenon. The red lines indicate those river locations missed out in the derived river network. It is due to the inevitable discrepancy between the original terrain and the induced terrain.
So we need some strategy to bias those given river locations. The goal is to make sure that all given river locations remain their river status.

## Slide 12: Biased river derivation - Details
Offer each given river location an initial water amount that is equal to the threshold amount.
  So they become river locations even without external water inflow
Protect them from being removed in the subsequent skeletonization process
  So they remain as river locations after the thinning process.
Notes: Our way is to offer each given river location an initial water amount that is equal to the threshold accumulation value right away. So they become river locations even without external water inflow.
Note that this practice doesn’t negatively affect their downstream locations – we know water comes out from those already-known river locations anyway.
Also, we protect them from being removed in the subsequent skeletonization process.

## Slide 13: Biased river derivation - result
Given river locations
River reconnection with biased river derivation
Notes: This slide shows the result after applying these two biasing measures. As you can see, we no longer miss any given river locations.

## Slide 14: Conclusion – Induced terrain solution framework
Guarantee given river locations must still be river locations
Honor given river locations as local minima w.r.t. non-river locations
Notes: So here is the the conclusion.
The key idea of this presentation is to introduce the induced terrain approach of completing fragmentary river networks. By first building up a terrain surface based on the partial observations, and then deriving a complete river network based on the induced terrain, we effectively impose the constraints imposed by the partial observations.
When this idea is put into practice, we find that in the first step of building up the terrain surface, the specific hydrological corrected terrain reconstruction scheme to use depends heavily on how the available height samples are distributed. If they are evenly distributed across the terrain, natural neighbor with stream burning is cost-effective in modeling the given river locations as local minima w.r.t. non-river locations.
For the second step, river network derivation, we find a need to bias those river locations to handle the unavoidable difference between the induced terrain and the original terrain. We give them sufficient amount of rain so they need not depend on inflow to get enough water accumulation; we protect them from being removed in the final skeletonization process. So they are guaranteed to be river locations.
The overall result is a river network that connects all the given segments together, and highly resembles the original river network.

## Slide 15: Terrain reconstruction (height samples only at river locations)
Typical terrain reconstruction with stream does not create inclined planes that
  grow to all possible directions
  get as far away as possible
Given river locations (with respective heights)
Reconstructed surface with typical terrain reconstruction scheme + stream burning
Desirable reconstructed surface
x
x
x
x
x
x
Notes: In our previous work, we assume height samples are available across the terrain, which is valid when the tree canopies are not that extensive. At that situation, we obtain reasonably good river reconnection results even if we stick with some conventional scheme, namely natural neighbor interpolation with subsequent stream burning. However, it no longer works in the much more adverse situation like what we have now.
To illustrate the problem, I am going to use this very simple 1D example on the right. It is a dataset with only two known river locations. Without height samples at the other locations, the terrain that we reconstruct with natural neighbor-stream burning is the middle one, a slope that goes upwards in general, with small bumps sitting exactly at the river locations. But what we really expect is something like the bottom one, inclined planes grow from each river location to all possible directions and get as far away as possible. With the middle terrain, we are likely to deduce river that goes from the right location to the left, which is obviously not the case if the terrain is actually the bottom one.

## Slide 16: Terrain reconstruction (height samples only at river locations)
Chaotic connections
Given river locations (black)
Missing river locations (light blue)
Reconstructed river network with NN-SB
Notes: We believe that it is such a terribly reconstructed terrain that leads to the serious river misroutes, as you see from the figure on the right.

## Slide 17: Our solution: ODETLAP
Basic version
  n2 unknowns {zi, j}
  Exact equations for all the k known-height positions
  Averaging equations for all n2 positions
  Weighting between the two sets of equations
Notes: To correct this problem, we propose replacing the terrain reconstruction scheme by the hydrology-aware version of ODETLAP. ODETLAP stands for Overdetermined Laplacian Partial Differential Equation. In basic ODETLAP we assume all height values in the terrain are unknowns, and we set up two groups of equations to solve for them. The first group are the exact equations available to all known-height positions. Each of them attempts to set the height of the location to the respective measured value. We claim it an attempt because they are competed by the second group of equations. They are available for all the positions. They are called averaging equations because each of them attempts to set the height of the respective position to the average of its immediate four neighbors, just like what we have in typical Laplacian Equations to make the surface smooth. Now we have n square + k equations for n square unknowns. The system is now overdetermined. The implication is that we normally don’t have a solution that satisfies all equations exactly. We can multiple both sides of an equation to increase its influence on the final solution. For example, if every averaging equation is multiplied by a factor R > 1, the solution will be biased towards terrain smoothness. The cost is to sacrifice measured value accuracy. That is to say, the solution at the known-height positions may deviate much more from the measured values.

## Slide 18: Our solution: ODETLAP
Hydrology-aware version (HA-ODETLAP)
  n2 unknowns {zi, j}
  Exact equations for all the k known-height positions
  Modified averaging equations for known river locs
    f = 1 if not given river location, > 1 otherwise
  Weighting between the two sets of equations
Notes: The hydrology-aware version of ODETLAP is based on the observation that at the river locations, its height should be smaller than any of its four neighbors rather than their average. To model this in ODETLAP, we change the averaging equations at known river locations: we set their reconstructed heights to be their respective neighborhood averages deflated by a certain factor f > 1. If f is large enough, the equations essentially set the reconstructed heights to values smaller than the respective neighbors.

## Slide 19: HA-ODETLAP effect illustrated
 |  |  | 10 |  |  |  | 
 |  |  | 10 |  |  |  | 
 |  |  | 10 |  |  |  | 
 | 10 |  |  |  | 10 | 10 | 10
10 |  |  |  |  |  |  | 
Given river locations and respective heights
Reconstructed terrain surface with stream burning
Reconstructed terrain surface with HA-ODETLAP
Notes: The power of HA-ODETLAP is on how it automatically models inclined planes that grow to all possible directions and extends as far as possible from the given river segments, even though we don’t have height samples around.
This slide shows a toy example. At the top, you see the known river locations and their respective heights. At the bottom left we see the reconstructed terrain with conventional terrain reconstruction scheme. It fails to assign inclined planes to positions which are just a bit away from the given river locations. The subsequent river derivation algorithm thus has a hard time figuring out how water at non-river locations should be routed.
In contrast, using hydrology-aware version of ODETLAP, we extend the inverted v-shape originating at the given river locations to as far away as possible, thus avoiding the problem.

## Slide 20: HA-ODETLAP
Much better connections
Reconstructed river network
Given river locations (black)
Missing river locations (light blue)
Notes: So with a much better terrain model, we can reconstruct the river segment connections better.